## Slide 1: An Improved Genetic Algorithm for bi-level multi-objective Q-Coverage in Directional Sensor Network
Nguyen Thi Hanh, Nguyen Van Son, Huynh Thi Thanh Binh, Ban Ha Bang, Trinh Van Chien
Notes: Hello everyone. My name is Hanh, I’m from Phuong Dong University, Vietnam.
Today, I will present about my research work named “An Improved Genetic Algorithm for bi-level multi-objective Q-Coverage in Directional Sensor Network”.

## Slide 2: Outline
Introduction
Related works
Problem Formulation
Proposed methods
Experimental results
Conclusion
Notes: My presentation contains 6 parts
as you can see in the slide.
Let’s move on to the first part, Introduction and background

## Slide 3: 1. Introduction
Wireless sensor network (WSN)
Notes: WSNs consists of two main components: a set of sensor nodes, scattered on the monitoring field and a base station. WSNs are applicable in many terrains and environments

## Slide 4: 1. Introduction
Applications in WSNs
Notes: WSN has many applications such as: smart city, Health care, Intelligent home, intelligent transportation service, smart building monitoring

## Slide 5: 1. Introduction
Advantage
  Saving cost
  Flexible deployment
  Applications
  …
Challenges
  Coverage
  Connectivity
  Fault - Tolerance
  Network lifetime
  …
Notes:   Wireless sensor networks with low cost, easy to deploy in variety conditions: topographic, environment, There are many major optimization criteria in constructing a WSN: Coverage
  Connectivity, Fault – Tolerance, Network lifetime
  This research focuses on optimizing target Coverage in DSNs

## Slide 6: 1. Introduction
Challenges of coverage
  Not enough coverage
  Weak security
  Unreliable information
Multi-coverage for each target
  Enhance sensor intensity
  Enhance coverage for important targets.
Target
Sensor
Focus on Q-coverage where each target has difference coverage requirements
Notes: There are a lot of challenges of coverage such as: …
To overcome these problems, we can deploy a sensor network that provides multiple layers of coverage for each target. This enhance sensor intensity and coverage for important targets.
Therefore, this research focus on Q-Coverage where in Q coverage each target has difference coverage requirements.

## Slide 7: 1. Introduction
A directional wireless sensor network is a type of network where sensors only monitor in a specific direction.
Q-coverage deployment enhance monitoring quality for each target.
Direction Sensor
Target
Q-coverage in Directional Sensor Network(DSNs)
Notes: Let talk about A directional sensor network.
This network is a type of network where sensors only monitor in a specific direction.
Q-coverage deployment enhance monitoring quality for each target.
Our paper focus on optimizing Q coverage in DSN.

## Slide 8: 1. Introduction
Cost of Deployment
Power Consuming
Fault-tolerant
Coverage Balancing
Coverage Quality
….
Challenges of Q-coverage in DSNs
Notes: There are many challenges of Q coverage in DSNs for example: …
In this research, we consider power consuming and coverage balancing
Where power consuming relate to the number of active sensors in network
And coverage balancing ensure coverage ratio of targets is balance to each other.
The two challenges that we address in this problem are energy optimization and coverage balancing for targets: In this context, energy optimization is achieved by minimizing the number of active sensors. Meanwhile, coverage balancing is achieved through balancing the coverage among the targets. We consider optimizing both objectives in two domains: under-provisioning and over-provisioning.
Under-provisioning is defined as a network where there is insufficient monitoring coverage by sensors
over-provisioning refers to a network where there is excessive monitoring coverage.
Hai thách thức mà chúng tôi address trong bài toán này chính là tối ưu năng lượng sử dụng, và tối ưu cân bằng bao phủ cho các targets. Trong đó tối ưu năng lượng tiêu thụ thông qua việc minizing số lươngj target sử dụng; còn cân bằng tải thì thông qua cân bằng bao phủ giữa các target. Chúng tôi xem xét tối ưu 2 mục tiêu trên, trong cả 2 miền under-provision and overprovison. Trong đó under-provision được định nghĩa là mạng thiếu sự giám sát của sensors, còn over-provision thì ngược lại.

## Slide 9: Outline
Introduction
Related works
Problem Formulation
Proposed methods
Experimental results
Conclusion
Notes: In this session, I present some related works:

## Slide 10: 2. Related works
[1] Formulate the Q-coverage problem with minimum sensors and high balance covered in DSNs:
  Proposed a Integer Linear Programming (ILP) model for simple solutions
  Proposed a Integer Quadratic Programming (IQP) formular to minimize the Euclidean distance between the required vector for coverage and obtained vector
  Proposed a Greedily-method to solve the minimizing IQP and maximum the balance in the network when under-provision
[2] Proposed two GA-based Algorithms to solve the Q-coverage problem with minimum sensors, and maximum the balancing coverage in DSNs:
  Focusing on ensuring the coverage of critical targets.
  Proposed Q-balancing Index metric to estimate the balancing of coverage in networks
[1] Al Zishan, A., et al., Maximizing heterogeneous coverage in over and under 916 provisioned visual sensor networks. 124 (2018) 44-62
[2] allah Mottaki, Nemat, Homayun Motameni, and Hosein Mohamadi. "A genetic algorithm-based approach for solving the target Q-coverage problem in over and under provisioned directional sensor networks." Physical Communication 54 (2022): 101719.
Notes: The first paper focuses on formulating the Q-coverage problem with minimum sensors and high balance covered in DSNs:
The authors proposed Integer Linear Programming, Integer Quadratic Programming and Greedily-method to solve the minimizing IQP and maximum the balance in the network
The second paper Proposed two GA-based Algorithms to solve the Q-coverage problem with minimum sensors, and maximum the balancing coverage in DSNs
  The proposed GA prioritize ensuring the coverage of critical targets and use QBI metric to estimate the balancing of coverage in networks

## Slide 11: 2. Related works
Disadvantage:
[1],[2] Only using the simply method to solve this problem. Therefore, the solutions are not effective.
[2] Proposed GA is not effective for both under-provision and over-provision domains.
Propose:
[1] Al Zishan, A., et al., Maximizing heterogeneous coverage in over and under 916 provisioned visual sensor networks. 124 (2018) 44-62
[2] allah Mottaki, Nemat, Homayun Motameni, and Hosein Mohamadi. "A genetic algorithm-based approach for solving the target Q-coverage problem in over and under provisioned directional sensor networks." Physical Communication 54 (2022): 101719.
An Improved GA to solve the Q-coverage problem with minimum number of sensor and maximum balancing.
The our proposed GA is effective for both under-provision and over-provision domains
Notes: But these related work also have some limits.

## Slide 12: Outline
Introduction
Related works
Problem Formulation
Proposed methods
Experimental results
Conclusion
Notes: this problem formulated as follows.

## Slide 13: 3. Problem Folmulation
Input:
  Surveillance region
  Set of directional sensor S = {s1, s2,…, sn}
  Set of targets T = {t1, t2,…, tm}
  The Q-coverage requirement: is the requirement sensors for each target
  Each sensor has the same:
    Sensing Radius:
    Angle of View:
Output:
  The number of active
  The direction of each sensors
Notes: The ta
vetor F is bisector- vector of the theta. And v is the vector from O to a target.

## Slide 14: 3. Problem Folmulation
Objective:
If the number available sensor is under-provision:
  Maximize the Q-balancing Index of networks (QBI): represent for the balance of
  the coverage rate/ the required coverage among sensors.
  If the number available sensor is over-provision:
  Minimize the number of active sensors (No.Active)
  Others metric considered: Power Consumming (PC), Distance Index (DI), Coverage Quality (CQ).

## Slide 15: Outline
Overview
Related works
Problem formulation
Proposed algorithm
Experiment results
Conclusion
Notes: Solving this model, we propose a bilevel objective Genetic Algorithm. The following are detail of this algorithm

## Slide 16: 4. Proposed Algorithm (SSD-IGA)
The steps of SSD-IGA
Individual representation
Fitness function
Population initialization
Genetic operator:
  Crossover
  Mutation
Selection operator
Notes: we propose an Improved Genetic Algorithm (IGA) to solve the Sensor Direction Determining (SDD) problem called SDD-IGA
. The outline of this algorithm is shown in the slide.

## Slide 17: Individual representation
Direction Sensor
Target
4. Proposed Algorithm (SSD-IGA)
Sensor |  |  |  |  |  |  |  | 
Sensor |  |  |  |  |  |  |  | 
State |  |  |  |  |  |  |  | 
State |  |  |  |  |  |  |  | 
Direction |  | 0 | 0 |  |  |  |  | 
Direction |  | 0 | 0 |  |  |  |  | 
Figure (a)
Figure (b)
Notes: Each solution is encoded as a chromosome having 2 parts:
Part one is the state of sensor: Active or inactive
Part two represent Direction sensor.
Is shown in the slide
the space of encodings is figure a and the space of solutions is figure b
1 lời giải được mã hóa thành 1 cá thể gồm 2 thành phần:
Active vector: alpha: trong đó alpha_i đại diện cho việc sensor thứ I trong lời giải được active hay không active.
Direction vector: omega: trong đó omega_i đại diện cho hướng quay của sensor thứ I trong lời giải.
Each solution is encode as a chromosome have 2 parts:
Active vector 𝛼, in this 𝛼_i is represent for i-th sensor in solution is active or inactive.
Direction vector omega, in this omega_i is represent for the orientation of –ith sensor.
=> with a chromosome c at this picture , we can decode to a deployment as a demo in this picture

## Slide 18: Fitness Function
Fitness function is represented by two parts: QBI and No.active sensors
If over-provision.
If under-provision
4. Proposed Algorithm (SSD-IGA)
Maximize QBI index first, then minimize active sensor index
Notes: Fitness function is represented by two parts: QBI and No.active sensors
when QBI equal to 1 and number active sensor is less than n then the domain is over provision
If QBI is less than 1 then domain is under provision
In this algorithm we Maximize QBI index first, then minimize active sensor index

## Slide 19: 4. Proposed Algorithm (SSD-IGA)
50% Randomly Initial:
  States of each sensor have a randomly status: active or inactive
  Direction of each sensor is randomly in
50% Heuristic Initial:
  States of a sensor is active if there is a target having distance to sensor < R other else inactive.
  Direction of each sensor is determined by the angle between the sensor and the nearest target
Population initialization:
Notes: To diversify the population, we employ two initialization strategies with a 50% random and 50% heuristic ratio.

## Slide 20: 4. Proposed Algorithm (SSD-IGA)
State gene: using multi-point crossover (shown in figure a)
Direction gene: using Greedily tuned SBX Crossover (shown in figure b)
Crossover operator
SBX
Greedily-tuned SBX with
Offspring1
Offspring2
Figure (a)
Figure (b)
Notes: Crossover operator have two parts:
State gene use multi-point crossover that is shown in figure a
Direction gene use Greedily tuned SBX Crossover that is given in figure b.
In this research we use Greedily tuned SBX Crossover in stead of basic SBX to focus on better genes. So, next generations can improve quality solutions

## Slide 21: 4. Proposed Algorithm (SSD-IGA)
State gene: one point mutation (shown in figure a)
Direction gene: Adaptive Polynomial Mutation based on coverage quality distance:
  if parents have good quality, offspring will have less differences compared to parents.
  If parents have bad quality, offspring will have more differences compared to parents.
Mutation operation
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
Figure (a)
Notes: Muation operator have two parts:
State gene: one point crossover.
Direction gene: Adaptive Polynomial Mutation based on coverage quality distance:
  if parents have good quality, offspring will have less differences compared to parents.
  If parents have bad quality, offspring will have more differences compared to parents.

## Slide 22: 4. Proposed Algorithm (SSD-IGA)
Selection operator
2
1
3
4
5
6
7
8
9
10
3%
11%
13%
7%
20%
9%
5%
9%
18%
5%
Selection operator is combination:
Roulette wheel selection
Elite selection technique
SPIN
SPIN
Individual | Value
1 | 3
2 | 11
3 | 7
4 | 20
5 | 9
6 | 5
7 | 9
8 | 18
9 | 5
10 | 13
Individual | Value
4 | 20
8 | 18
10 | 13
2 | 11
5 | 9
7 | 9
3 | 7
6 | 5
9 | 5
1 | 3
Elite 10%
Notes: The selection is Combination of:
  In Roulette wheel selection
  The individual have better fitness value it will have more chance to be selected to next generations

## Slide 23: Outline
Introduction
Problem Formulation
Related works
Proposed methods
Experimental results
Conclusion

## Slide 24: 5. Experiments and Results
Scenario 1: 9 Datasets
- Same radius:
- Same number of targets: 130 nodes
- Number of sensors: [20,180] with a jump of 20 nodes.
Scenario 2: 8 Datasets
- Same radius:
- Same number of sensors: 100 nodes
- Number of targets: [10,150] with a jump of 20 nodes.
Scenario 3: 7 Datasets
- Same number of sensors: 100 nodes
- Same number of targets: 130 nodes
- Radius from with a jump of
Problem instances

## Slide 25: 5. Experiments and Results
Algorithm Parameters:
Parameters | Values
The Angle of View | 
Coverage constraints | 
Crossover rate | 0.8
Mutation rate | 0.1
Population size | 100
Maximum Generation | 1000
Number of converge iteration | 100
Parameters | Values
The Angle of View | 
Coverage constraints | 
Crossover rate | 0.8
Mutation rate | 0.1
Population size | 100
Maximum Generation | 1000
Number of converge iteration | 100

## Slide 26: 5. Experiments and Results
Experiment 1: The effect of the number of sensors on the performance of the algorithms
SDD-IGA required 101% the number of sensor active compared to DSGA but yielded better QBI (262%), DI (8%) and CQ (14%)

## Slide 27: 5. Experiments and Results
SDD-IGA is better than 231% and 6% for QBI and DI. Moreover, SDD-IGA also produces better results than DSGA in terms of number of sensor active and PC.
Experiment 2: used the under-provisioned dataset to evaluate the impact of target numbers on QBI and the Q-coverage ability DI

## Slide 28
5. Experiments and Results
Experiment 3: In an under-provisioned environment (sensing range R 90m), focused on comparing QBI and DI of the three algorithms
SDD-IGA outperform both SGA and DSGA on these metrics. Specifically, SDD-IGA beats SGA by 25% on QBI and 18% on DI. SDD-IGA is better than DSGA 297% on QBI.

## Slide 29: 6. Conclusion
Contribution:
  Proposed SDD-IGA for both over-provisioned and under-provisioned environments.
  Various experiments based on multiple scenarios
  Ours technique could efficiently solve problems and outperform the latest works
  Testing the “health” hypothesis with SDD-IGA algorithm and demonstrate it is effective to improve the solution
Future works:
  Expanding our research to deal with the simultaneous placement of sensors and adjustment of the orientation angle of the sensors
  Real-time coverage for moving targets
Notes: In this work, we study the Q-coverage problem, which is one of the main challenges in DSNs: